## Slide 1
GUJARAT POLICE · SENTINEL INNOVATION CHALLENGE 2026
Sentinel
One pane of glass over a heterogeneous camera estate:
follow one vehicle across 26 departments that do not share a system.
371 automated tests · 11 database migrations · 45 API operations
Every figure in this deck is produced by a script in the repository.
Notes: Open by naming the problem, not the technology. 26 departments own cameras and cannot see each other's. Everything else follows from that.

## Slide 2
THE PROBLEM
A vehicle crosses a boundary, and disappears
26
police departments own cameras in Gujarat
None can see another's estate. A vehicle leaving Ahmedabad for Surat leaves the record.
4
protocols, 9 vendors, in one real estate
18% analog on legacy DVRs. 10% municipal HLS at 10-second latency. A system that needs clean modern IP has not solved the problem.
~20%
of a real estate is dead at any moment
Frozen, misaimed or offline. A dashboard that hides this trains officers to trust what they should not.
Notes: Do not rush this slide. The judges know these facts. Showing that you know them buys the rest of the talk.

## Slide 3
CONSTRAINT 1 OF 3
Video never centralises. Metadata does.
80,000 cameras at 4 Mbps is not a budget problem. It is physics, and no centralised design survives it.
Centralise the video
320 Gbps
104 petabytes per month of state backbone
Centralise the answer
96 Mbps
~5 kbps per camera of structured sightings
A factor of 3,300. Video stays at the edge; clips are pulled on demand. Every other architectural decision follows from this one.
Notes: This is the slide that decides whether the architecture is credible. 320 Gbps is not affordable at any budget.

## Slide 4
ARCHITECTURE
Edge decides. Regional joins. Central remembers.
EDGE
At each district
Decode (NVDEC)
Detect · YOLOX
Track · ByteTrack
Quality gate ~80% out
ANPR + ReID + colour
Video stays here. Permanently.
REGIONAL
A few per state
Cross-camera matching
Spatio-temporal gate
Alert rules
Vehicles cross districts, not states.
CENTRAL
Gandhinagar
Registry & map
Search & tracking
RBAC & audit log
Metadata only. ~5 kbps/camera.
Browsers fetch video directly from the media server over WebRTC. Video never crosses the edge/core boundary except as an on-demand clip.

## Slide 5
CONSTRAINT 2 OF 3
The gate matters more than the model
Given a sighting, only cameras reachable by road in a plausible travel window are candidates. It is a PostGIS query against a cached routing matrix — no GPU, no model.
Chart: Comparisons for one batch (50 sightings x 400 vehicles)
| Without the gate | With the gate
Pairs scored | 20000 | 473
97.6%
fewer comparisons
2,240 ms -> 53 ms
scoring time for one batch
112 microseconds
measured cost per scored pair
Why it matters: appearance matching at a 0.9% false-positive rate is unusable against 49 cameras and trustworthy against 3.
Notes: If a judge asks what the gate is worth in compute rather than in candidates: this slide is the answer, and the matcher counts both in production so it is checkable on a running system.

## Slide 6
CONSTRAINT 3 OF 3
ANPR alone cannot track a real estate
Chart: Correct plate, as a share of all attempts (%)
| ANPR lane, day | ANPR lane, night | Surveillance, day | Surveillance, night | Wide-angle, 58px
End-to-end accuracy | 92.5 | 79 | 75.6 | 37.9 | 11.2
26%
of the estate can physically resolve a plate. Below ~55 px of plate width nothing works — that is optics, not tuning.
So we fuse three signals
Plate — precision
Appearance (ReID) — recall
Attributes — colour, type
We publish our worst number because an officer needs to know when not to trust the system.

## Slide 7
TRUSTWORTHINESS
Appearance can never confirm a match
1
CONFIRMED
Plate matched, and travel time is physically possible against the road distance. Camera 14 to 22: 610 m in 47 s = 47 km/h.
2
PROBABLE
Appearance and attributes agree inside the gate, but no plate was read. Score ceiling 0.79 — it can never reach CONFIRMED.
The ceiling is a safety property, not a tuning choice
A system that identifies a car by colour and shape will eventually identify the wrong car, and an officer will act on it. A rejected match is shown too: same plate read, but the travel time implied 180 km/h on an urban road — physically impossible, so it is not a match, whatever the appearance score said.
The full score breakdown is one click away on every hop. The false-positive rate is displayed, not hidden.

## Slide 8
SECURITY
We attacked our own system
26 departments share one database. Isolation is the control that makes that acceptable — so we tested it adversarially against a live two-department estate rather than asserting it.
18
authorisation findings, each proved by an exploit that ran
18
fixed and held by 18 regression tests written as attacks
0
SQL injection, algorithm-confusion or secret-handling faults found
The finding that mattered most
An operator in one department could acknowledge another department's CRITICAL stolen-vehicle alert — a write, not a leak. Twenty-five earlier tests passed throughout, because all twenty-five tested cameras. Scoping the registry is not scoping the estate.
Notes: This slide wins trust. Nobody else will show a slide of their own security failures. The point is that we found them ourselves, before deployment, and can prove each fix.

## Slide 9
RESILIENCE
Failover is tested, not described
A police evidence store that loses the last N minutes on a primary failure has lost evidence, not throughput. So we ran the drill rather than writing the policy.
0
records lost — observed RPO
0.36 s
kill to accepting writes — observed RTO
0.27 s
streaming replica catch-up
What the drill actually does
Builds a primary with WAL archiving and a streaming standby with a replication slot
Writes 5,000 evidence rows, then kills the primary with no clean shutdown — the closest a drill gets to losing power
Promotes the standby, counts what survived, and confirms it accepts new evidence
Archives WAL segments, so point-in-time recovery covers a bad write noticed an hour later
Run it yourself: python scripts/dr_drill.py

## Slide 10
PRIVACY & LAWFULNESS
In the schema, not the roadmap
Purpose limitation
Viewing a vehicle's movement history requires a stated purpose, recorded to a 7-year audit log. DPDP Act 2023 makes this an obligation, not a preference.
Audited refusals
Reading the audit log is itself audited. An attempt to reach another department's camera is recorded with who tried — a refusal that leaves no record is one an attacker can retry all year.
No password can be stored
No column in the database can hold a camera credential. Credentials are referenced by name and resolved from a secret store; inline passwords are refused outright in production.
Minimum disclosure
Screening a plate releases a status flag and nothing else — not the owner's name or address. Owner details need a registered investigation with a case reference.
It also runs air-gapped: no font CDN, no map token, no external model service. When the tile server is unreachable the overlays still render — the correct degraded behaviour for a control room, and it is tested.

## Slide 11
STATUS
What is proven, and what is not
Every requirement maps to an implementation, a named test and a status. If you challenge a claim in this deck, we will show you the line and the test that holds it.
✓
Tested and executed
Full pipeline: decode, detect, track, ANPR, ReID
Cross-camera matching under the road-network gate
Department isolation across every data surface
Audit log, purpose limitation, RBAC
Failover: 0 records lost, 0.36 s recovery
Live RTSP: TCP pinned, PTS timing, reconnect backoff
!
Not done — stated plainly
Never run against the real Sentinel gateway
No government record system is connected — all five adapters are mock, and every record is stamped
Accuracy figures are the simulator's, not real Gujarat imagery
Not executed above 1,000 cameras — beyond that every figure is arithmetic over stated assumptions
We are not calling this production ready. We would rather you heard that from us than found it afterwards.
Notes: Do not skip this slide and do not soften it. It is the reason to believe every other number in the deck.

## Slide 12
STATEWIDE ROLLOUT
Five phases, each with entry criteria
1
Pilot
50–200
M1–6
2
District
3,000
M6–14
3
Metro
12,000
M12–24
4
Highway
25,000
M20–32
5
Statewide
80,000
M30–40
Infrastructure at 80,000
~500 edge nodes carrying ~2,000 GPUs. The GPU is the binding constraint at ~40 cameras each — decode is 7x cheaper than inference. 24 PB of hot video stays at the edge and never moves.
What must be true before Phase 1
Real gateway integration · measured ANPR accuracy on real imagery · authorised government record access · a thermally qualified edge appliance. Each is currently unmet, and each is named in the rollout plan.

## Slide 13
COST
Federated against centralised, year one
Chart: Year-one cost, Rs crore
| Federated (Sentinel) | Centralised
Year-one cost (Rs crore) | 82.7 | 138.7
Rs 56.0 crore
difference in year one. Storage and backbone alone account for Rs 57.6 crore of it.
!
Read this as an estimate
No procurement quote was obtained. Unit costs are estimates against list prices, and every one of them is labelled as such in the cost model. We would expect a tender to move these numbers.
Method and every unit cost: docs/COST_BENEFIT.md

## Slide 14
WHAT WE ARE ASKING FOR
Access, and a pilot
1
Sentinel gateway credentials
Host, credentials and API documentation. Our preflight tool answers your integrator checklist on the day we receive them.
2
Real imagery for one camera class
So the accuracy we publish is Gujarat's, not a simulator's.
3
A 50–200 camera pilot district
Phase 1. Every entry criterion is written down, and we will report against it honestly.
371 tests · 11 migrations · 45 API operations · every requirement traced to a named test
Notes: Close on the ask, not on a summary. The three things you need are access, imagery and a pilot district.